## Slide 1
Predictive Maintenance
with Edge ML on NuttX
TensorFlow Lite Micro | STM32F407 | Renode
Onwukanjo Innocent (202487225)
ENGI 9875 — Memorial University | April 2026

## Slide 2
The Problem
Unplanned Failures
Threshold-based monitoring misses subtle degradation patterns
Cloud inference adds latency and network dependency
Need: on-device ML with real-time guarantees
Our Approach
Train a neural network classifier offline (Keras)
Quantize to INT8, deploy via TFLite Micro
Run inference directly on STM32 under NuttX RTOS
What It Detects
Normal Motor: 5 Hz sine wave (smooth bearing)
Bearing Fault: 20 Hz whine (degraded bearing)
2,608
bytes model
708
bytes RAM

## Slide 3
Built With
NuttX RTOS
POSIX-compliant RTOS for ARM Cortex-M4. Provides pthreads, mqueues, semaphores.
TFLite Micro
Edge inference engine for INT8 quantized models. Runs with <1 KB runtime RAM.
STM32F407
ARM Cortex-M4 target. 1 MB Flash, 192 KB SRAM. Simulated in Renode.
Python / Keras
Offline model training: binary classifier (Dense 16 ReLU → Dense 1 Sigmoid).

## Slide 4
System Architecture
Sampling Task
Priority 110
100 Hz periodic reads
Quantize to INT8
Send via mqueue
Inference Task
Priority 100
Receive from mqueue
Run TFLite Micro
Score anomaly
Alert Task
Priority 90
Block on semaphore
Wake on anomaly
Log & alert
→ mqueue →
→ sem_post →
Shared Anomaly Log (semaphore-protected)

## Slide 5
Learning Outcomes
LO1
Real-Time Scheduling
Three tasks with Rate-Monotonic priority assignment (110/100/90). Total utilization U = 0.180, well below the RMS bound of 0.780.
LO3
Concurrency
Shared anomaly log accessed by inference (write) and alert (read) tasks. Protected by POSIX semaphore to prevent data corruption.
LO5
Device Interface
Sampling task mirrors a driver pattern: periodic reads → structured packets → inter-task channel. Full char driver is future work.

## Slide 6
RTOS Services in Action
POSIX Message Queue
/ml_vib_queue with 5-msg capacity. sensor_batch_t packets (10 INT8 readings + metadata). Decouples sampling from inference.
Counting Semaphore
g_log_sem (init=1) protects the shared anomaly log. Both inference and alert tasks acquire before access. Minimal critical section.
Task Notification
g_alert_sem (init=0) — alert task blocks on sem_wait(). Inference calls sem_post() on fault detection. Zero-overhead when no anomaly.
Priority Scheduling
Sampling=110, Inference=100, Alert=90. Preemptive. Sampling never starved. Alert only runs when signaled.

## Slide 7
Results
100%
Classification
Accuracy
20/20
Batches
Correct
138 KB
Flash
Usage
708 B
Arena
Used
Batch Range | Signal | Expected | Result
0 – 9 | 5 Hz sine | NORMAL | 10/10 OK ✓
10 – 19 | 20 Hz whine | FAULT | 10/10 FAULT ✓
All 10 normal batches classified correctly. All 10 fault batches triggered anomaly alerts.

## Slide 8
Challenges
NuttX ↔ TFLite C++ Math Incompatibility
TFLite expects std::round, std::pow, etc. NuttX only provides C math.h without std:: namespace or float overloads. Built a 90-line compatibility shim (nuttx_math_shim.h) handling namespace injection, float overloads, macro wrapping, and overload ambiguity.
Function Pointer Type Mismatches
TFLite passes std::sin as float(*)(float), but NuttX only has double sin(double). Added inline float overloads to the shim to provide exact type matches.
Linker: Missing MicroPrintf Symbol
TF_LITE_STRIP_ERROR_STRINGS compiled out MicroPrintf but the op resolver still referenced it. Fixed by enabling CONFIG_TFLITEMICRO_DEBUG.
Entry Point Naming
NuttX expects <progname>_main with extern "C" linkage. Standard main() causes an undefined reference at link time.

## Slide 9
Future Improvements
Character Device Driver
Implement /dev/accel0 as a NuttX char driver so sampling task uses open()/read() — completing LO5.
Autoencoder Model
Replace binary classifier with an autoencoder for unsupervised anomaly detection — no labeled fault data needed.
Physical Hardware
Deploy on real STM32F4 Discovery with MEMS accelerometer (LIS3DSH) for live vibration data.
FFT Features
Add frequency-domain analysis before inference for better discrimination of complex fault signatures.

## Slide 10
Live Demo & Questions
Renode → NuttX Shell → pred_main_ml
Onwukanjo Innocent | 202487225 | ENGI 9875